## Slide 1: Deep Learning for Vessel Segmentation in Cerebral CTA
A Controlled Ablation of Topology-Aware Loss Functions
Samih Tharwat Amer | Whiting School of Engineering – Johns Hopkins University | EN.525.733 Dr. Nasrabadi

## Slide 2
What is a CTA?
Regular CT
CTA
Computed Tomography (CT): X-ray based imaging that produces cross-sectional 3D volumes of the body
CT Angiography (CTA): A CT Scan where a patient is injected with a contrast dye that highlights blood vessels
Regular CT: Shows bone and soft tissue – vessels are nearly invisible
CTA: Contrast fills the vasculature, making arteries brighter
This is the imaging modality of choice for stroke triage and aneurysm detection

## Slide 3: Clinical Motivation
Cerebrovascular Diseases
  Leading cause of death and disability worldwide. Accurate vessel segmentation from CTA is essential for diagnosis and surgical planning
Circle of Willis (CoW)
  The arterial anastomotic ring at the brain’s base. Provides collateral blood flow pathways critical during vascular occlusion.
Communicating Arteries (Acom, Pcom)
  Thin (<1mm diameter) but clinically critical for aneurysm assessment and collateral flow. Most prone to segmentation failure.
Notes: "Cerebrovascular diseases — stroke, aneurysms, arteriovenous malformations — are a leading cause of death and disability worldwide. Accurate segmentation of cerebral vasculature from CT angiography is essential for diagnosis and surgical planning."
So why do we need automated vessel segmentation? Today, if a neurosurgeon wants a 3D map of a patient's cerebral vasculature — for surgical planning, aneurysm assessment, or stroke triage — a radiologist has to manually trace the vessels slice by slice. That takes hours per scan. It's simply not feasible in an emergency setting where treatment decisions need to happen in minutes.
"Automated segmentation changes that. It can turn a raw CTA scan into a 3D vascular model in seconds, enabling real-time surgical navigation, 3D aneurysm visualization, and rapid collateral flow assessment during
stroke triage.“ "The primary region of interest is the Circle of Willis — the arterial ring at the base of the brain. It has large named arteries — ICA, MCA, basilar — but the thin communicating arteries, the Acom and Pcom, are what matter most. These are the collateral pathways. When a major vessel is blocked during a stroke, whether the patient has intact communicating arteries determines whether blood can reroute. If your segmentation misses or disconnects these, the clinical utility is lost."

## Slide 4: The Problem – Topological Failures
Deep learning segmentation models optimize for voxel overlap – no concept of vessel connectivity
A segmentation can score DSC 0.87 while containing severed vessels and disconnected fragments
Aggregate metrics are misleading – dominated by large, easy arteries; hide failures on thin structures
Clinically useless segmentations can look numerically acceptable
Global DSC: 0.87 R-Pcom DSC: 0.42 L-ACA DSC: 0.46
Notes: "Here's the core problem. Current deep learning segmentation models are optimized to maximize voxel-level overlap with the ground truth. They have no concept of whether a vessel is connected end-to-end or whether
▎ it's been severed into fragments. A segmentation can score a Dice coefficient of 0.87 (that's the standard overlap metric, essentially measuring what percentage of predicted vessel voxels match the ground truth) — which sounds excellent — while containing completely broken vessels."
▎
▎ "When we actually tested our first model in a clinical 3D viewer, this is exactly what we found. The global metrics looked reasonable, but when we broke it down by individual vessel class, the posterior communicating
▎ artery scored 0.42, and other communicating arteries were similarly poor. The aggregate score was dominated by the large arteries — the ICA, MCA, basilar — which are easy to segment. The thin structures that matter
▎ most for clinical decisions were failing silently."
▎
▎ "So the question becomes: can we train these models to care about connectivity? That's where topology-aware loss functions come in, which we'll get to shortly."

## Slide 5: The TopCoW Challenge
Evaluation Protocol
Dice Score (DSC)
Voxel overlap between prediction and ground truth
Centerline Dice (clDice)
Skeleton-level overlap — topology agreement
HD95 (mm)
95th percentile Hausdorff distance — surface accuracy
Betti-0 Error
Connected component mismatch — topological correctness
Challenge Overview
MICCAI 2024 Challenge
Topology-aware anatomical segmentation of the Circle of Willis for CTA and MRA
125 CTA + 125 MRA volumes
Expert voxel-level annotations for 13 vessel classes
Key finding from challenge:
Even top teams achieve good aggregate Dice while producing topologically incorrect segmentations
Notes: Our work builds on the TopCoW 2024 Challenge — a MICCAI challenge specifically designed to benchmark Circle of Willis segmentation. The challenge provides 125 CTA and 125 MRA volumes with expert voxel-level annotations for 13 vessel classes. What makes TopCoW unique among segmentation challenges is its evaluation protocol: beyond standard Dice and Hausdorff distance, it measures topological correctness using the Betti-0 error — which counts connected component mismatches between prediction and ground truth — and centerline Dice, which evaluates skeleton-level overlap."
>
> "The key finding from the TopCoW challenge is that even top-performing teams achieve good aggregate Dice scores while still producing topologically incorrect segmentations. The communicating arteries, which are the most clinically important structures in the Circle of Willis, remain the weakest point across all submitted methods. This motivated our study: can we specifically improve topology through the loss function alone?"

## Slide 6
Related Work & State of the Art
Segmentation Backbone
nnU-Net
Isensee et al., Nat. Methods 2021
Self-configuring 3D U-Net. Established Dice+CE as standard. Dominant framework.
nnU-Net Revisited
Isensee et al., MICCAI 2024
Call for rigorous validation in 3D medical image segmentation.
Topology-Preserving Losses
clDice
Shit et al., CVPR 2021
Differentiable soft-skeletonization. First topology-preserving loss for tubular structures.
Skeleton Recall
Kirchhoff et al., ECCV 2024
CPU-precomputed skeletons. Efficient centerline recall.
CBD-Loss
Shi et al., MICCAI 2024
Joint centerline + boundary optimization.
Other Approaches
Persistent Homology
Berger, Stucki (MICCAI/ICML)
Topological loss via persistence barcodes.
NexToU
Shi et al., 2023
Topology-aware U-Net architecture.
Cascaded U-Net
Rougé et al., PLOS ONE 2024
Topology-aware multi-task approach.
Gap: Existing evaluations confound loss function effects with architectural changes or aggregate-only challenge metrics
Notes: "The backbone of modern medical image segmentation is nnU-Net by Isensee et al., published in Nature Methods 2021. It established the Dice plus cross-entropy paradigm that nearly all top methods build on. In 2021, Shit et al. at CVPR introduced centerline Dice — clDice — which computes Dice on morphological skeletons using differentiable soft-skeletonization. This was the first loss function to directly penalize topological disconnection in a differentiable way."
>
> "More recently, Kirchhoff et al. at ECCV 2024 proposed Skeleton Recall, which takes a more computationally efficient approach — precomputing binary skeletons on CPU and using them as attention masks. Other related work includes the Centerline Boundary Dice loss from Shi et al. at MICCAI 2024, methods based on persistent homology from Berger and Stucki, and specialized architectures like NexToU."
>
> "The key limitation we identified is that existing evaluations of these topology-aware losses either introduce them alongside architectural changes — making it impossible to attribute improvements to the loss function alone — or they report only aggregate scores on multi-team challenge leaderboards. Our work addresses this gap through a controlled, single-variable ablation."

## Slide 7
Hypothesis & Approach
HYPOTHESIS
Topology-aware loss functions will disproportionately improve
segmentation of thin communicating arteries (Acom, Pcom)
Config 1
Dice + CE
Baseline — overlap only
nnU-Net default
Config 2
Dice + CE + clDice
Centerline matching
Shit et al., CVPR 2021
Config 3
Dice + CE + Skeleton Recall
Centerline recall
Kirchhoff et al., ECCV 2024
Controlled ablation: same architecture, same data, same hardware — only the loss function changes
Notes: "Our hypothesis is that topology-aware loss functions will disproportionately improve segmentation of thin communicating arteries — the Acom and Pcom — which are most prone to topological failure."
>
> "To test this cleanly, we designed a controlled ablation. We hold everything identical — the same 3D U-Net architecture, the same data splits, the same hardware, the same optimizer and hyperparameters — and vary only the loss function. Three configurations: first, Dice plus cross-entropy as the baseline; second, adding soft centerline Dice from Shit et al.; and third, adding Skeleton Recall from Kirchhoff et al. Both topology-aware terms are combined with the base loss at equal weight, alpha equals 0.5."

## Slide 8: Datasets
TopCow 2024
MICCAI Challenge Dataset
125 CTA volumes with expert annotations
13 Circle of Willis vessel classes
100/25 train/validation split (80/20)
Classes: BA, ICA, MCA, PCA, ACA, Acom, Pcom, 3rd-A2
Used for: From-scratch training
TopBrain 2025
Extended Annotations – Same Scans
25 CTA Volumes (same scans as TopCow subset)
40 vessel classes – 2x more coverage
New: Distal branches, posterior fossa, small arteries, venous sinuses
Binarized: GT covers far more vasculature
Used for: Fine tuning and transfer evaluation

## Slide 9: Architecture: 3D U-Net
Encoder 5 stages: 32 → 64 → 128 → 256 → 512 ch
Blocks: 2x Conv3D(33) + InstanceNorm + LeakyReLU (α=0.01) + residual
DownSampling: Strided 23 convolutions (learnable, no max-pool)
Upsampling: Transposed convolutions + skip connections (concat)
Deep Supervision: 1x1 heads at each decoder level, weights: 1.0, 0.5, 0.25, 0.125
Parameters: 24.9M (Kaiming normal init)
Design: nnU-Net philosophy (Isensee et al., 2021)
Why 3D U-Net? Strongest controlled baseline — any performance difference attributable to the loss function, not the architecture

## Slide 10: Loss Functions: Dice + Cross-Entropy (Baseline)
Soft Dice Loss
pi = predicted probability at voxel i
gi = ground truth label at voxel i
ɛ = 10-5 (numerical stability)
Measures region-level overlap. Per-class computation (excluding background), then averaged
Cross-Entropy Loss
Standard per-voxel classification loss. Provides sharp gradients for individual voxel decisions.
Limitation: Every voxel receives equal weight. A centerline voxel of a 1mm Pcom gets the same gradient as a surface voxel of the 5mm ICA.

## Slide 11
Loss Functions: Soft Centerline Dice (clDice)
Differentiable Soft-Skeletonization
Topology Metrics
Combined:
Intuition: Computes skeletons (centerlines) of both prediction and ground truth, then measures how well they overlap. Directly penalizes topological disconnection — if the prediction's centerline doesn't match the ground truth's centerline, the loss increases. Measures both precision (predicted skeleton inside GT) and sensitivity (GT skeleton covered by prediction).

## Slide 12
Loss Functions: Skeleton Recall
Skeleton Recall Loss
skel(y) = precomputed binary skeleton (CPU, scikit-image)
ŷ = predicted vessel probability map
α = 0.5
Key Differences from clDice
CPU precomputation
No GPU-intensive iterative operations
Recall only
Does not measure prediction skeleton precision
Binary skeleton
Exact morphological thinning, not soft approximation
Computationally efficient
~13% overhead vs baseline
Intuition: "Did you find the core of every vessel?" Precomputes a 1-voxel-wide centerline of the ground truth, then asks how much of this skeleton the prediction covers. Focuses all gradient signal on centerline voxels — even at the cost of over-segmentation. The base Dice+CE handles false positives; Skeleton Recall ensures the thinnest structures aren't missed.
Summary of Loss Functions
Loss | Topology Signal | Computation | Trade-off
Dice+CE | None | Fastest | No topology awareness
+ clDice | Precision + Recall | GPU-intensive (K=10 iters) | Best aggregate metrics
+ Skeleton Recall | Recall only | CPU precompute (+13%) | Best thin-vessel detection

## Slide 13: Training Setup
Hardware
8× NVIDIA A100-SXM4-40GB (AWS p4d.24xlarge)
Training
DDP across all 8 GPUs — identical for all 3 models
Epochs
300 (from-scratch) | 150 (TopBrain fine-tuning)
Optimizer
AdamW (LR = 10⁻³, weight decay = 10⁻⁵)
LR Schedule
Cosine annealing + 10-epoch linear warmup (10⁻⁷ → 10⁻³ → 10⁻⁷)
Patches
128³ voxel crops, 4 per volume, 33% foreground-centered
Batch Size
4 per GPU (32 effective) | Mixed precision (AMP)
Validation
Every 25 epochs | Early stopping patience = 5 cycles
Fine-tuning
Best checkpoint, fresh optimizer, LR = 10⁻⁴, 5-epoch warmup
All training configuration identical across runs — controlled single-variable comparison

## Slide 14
Training Dynamics
All three models converge to similar regions:
Training loss: ~0.10–0.13
Validation Dice: ~0.84–0.86
clDice and Dice+CE are nearly identical
Skeleton Recall runs at slightly higher loss — expected from additional centerline penalty
Stable convergence across all configurations. No NaN batches.

## Slide 15
Global Results — From Scratch
clDice wins aggregate
DSC 0.864 | clDice 0.916
Lowest Betti-0 error: 3.72
Baseline close behind
DSC 0.858 | clDice 0.907
Betti-0 error: 5.76
Skeleton Recall
Lower aggregate (DSC 0.845)
High B0 error: 26.84 (over-segments)

## Slide 16
Stratified Results — The Vessel Gap
Skeleton Recall → Pcom Improvement
R-Pcom: 0.511 vs 0.459 baseline (+5 pts)
L-Pcom: 0.479 vs 0.410 baseline (+7 pts)
Vessel Gap Analysis
Model | Large | Comm. | Δ
Dice+CE | 0.795 | 0.433 | 0.363
+ clDice | 0.797 | 0.435 | 0.363
+ Skeleton | 0.798 | 0.466 | 0.332
Hypothesis partially supported: modest but targeted improvement on communicating arteries

## Slide 17
TopBrain Fine-Tuning — The Big Result
SMALL ARTERIES
(Ophthalmic, Ant. Choroidal)
0.589
Skeleton Recall
0.000 Dice+CE
0.000 clDice
Posterior fossa:
0.626 vs 0.565 (Dice+CE)
Venous sinuses:
0.613 vs 0.416 (Dice+CE)
Distal branches:
0.752 vs 0.687 (Dice+CE)
Large CoW:
all ~0.82 (comparable)
Skeleton Recall finds vessels the others cannot — a qualitative, not merely quantitative, difference

## Slide 18
Qualitative Comparison — 3D Renderings
[SurgicalAR Screenshot]
Dice+CE + TopBrain
[SurgicalAR Screenshot]
Skeleton Recall + TopBrain
Same patient | Same viewing angle | Same fine-tuning protocol | Different loss during pretraining

## Slide 19
Discussion — What We Learned
clDice
Best Aggregate Model
DSC 0.864 | Betti-0 error 3.72
Improves topological precision
Fewer disconnected fragments
Best for: overall segmentation quality
Skeleton Recall
Best Thin-Vessel Transfer
Pcom: +5–7 pts | Small arteries: 0.589
Improves topological recall
Over-segments (B0 error 26.84)
Best for: finding every vessel
KEY INSIGHT
TopBrain fine-tuning drives comprehensive vessel coverage for all models.
The loss function used during pretraining shapes the quality of that transfer to the thinnest structures. Skeleton Recall's centerline-focused gradient signal creates feature representations that encode thin tubular geometry — a representational advantage that transfers when exposed to richer annotations.

## Slide 20
Limitations & Future Work
Limitations
Large-small vessel gap persists
>0.33 DSC across all models
Skeleton Recall over-fragments
Betti-0 error 26.84 needs post-processing
HU window [0, 600]
Clips bone to same range as vessels → false positives
Future Work
Wider HU window [0, 1500]
Separate bone from vessels — highest-impact fix
Class-balanced sampling
Focus on under-represented thin vessels
Connected component filtering
Remove small disconnected false positives
Retrain on corrected labels
50 model-assisted labeled CTAs on RedBrick AI

## Slide 21
Conclusion
Controlled ablation on identical hardware
3 loss functions, same 3D U-Net, same 8× A100 configuration
clDice = best aggregate model
DSC 0.864, lowest Betti-0 error 3.72, best topological precision
Skeleton Recall = best thin-vessel transfer
+5–7 pts on Pcom, 0.589 on small arteries vs zero for alternatives
Topology-aware pretraining creates better representations
Loss function during pretraining shapes how well coverage transfers to thinnest structures
Hypothesis partially supported
Modest CoW improvement; dramatic effect on truly small vessels after transfer
The large-vs-small vessel gap remains the central challenge — the arteries that matter most clinically are the hardest to find.

## Slide 22
Thank You
Questions?
Samih Tharwat Amer
Whiting School of Engineering | Johns Hopkins University